To download the extension

- Go to ESRI.com

- Click on the Support tab and Downloads

- Search for GPSi

- Click on Downloads

- READ the directions (incase you have any errors)

- Download and unzip file

- Open the README file and follow the directions

- Add the toolbar to ArcMap

  - Click on View/Toolbars/ GPSi

- Connect your GPS unit to the computer and turn the unit on.

- On the GPSi toolbar

  - Click GPS Interface

  - Click GPS Connection Properties to check the connection

  - Click Waypoints/ Download Waypoints

  - Select the waypoint you want or Select All

  - Click on Save and navigate to where you want to save the shapefile.

  - The new file will be automatically added to the map.