## Slide 1: Local Drop off boxes
Nov 12, 2020. Utah CBRS/LTE User Group

## Slide 2: 3GPP CUPS – Control and user plane separation
The EPC core process all control plane traffic
Call setup
Radio management
Typically a few kb of data
The Local Drop Off Box processes the data
The information you pass through LTE
Configured to be a part of your private network
The bulk of the data

## Slide 3: What is the drop off box (media gateway)
Drop off box for user plane traffic
VMWare compatible Linux Appliance
Comes pre-configured as an OVA file
Needs to see the radio VLAN (connects to the EPC Core)
Needs to see an internal VLAN on your network (this is where it drops off)

## Slide 4: TCP/IP configuration options – on your side
Address Range
NAT

## Slide 5: nat
Only requires a single ip address inside your network
Address can be public or private
All traffic is comes from that address
Private addresses used “inside” the gateway are assigned to your UE devices (MiFi and Bai Cells)
All traffic on the iBoss has the same IP address
Devices behind the NAT are not accessible from outside the gateway except through the port translation

## Slide 6: Address range
IP Subnet from your network
  Can be public or private
  Recommended to be filtered and firewalled
The Media Gateway has to route traffic by design
    You need to be able to split up the subnet
    You may need static routes on your switches/routers
Allows traffic to flow both directions
    You can remote into MiFi or Bai Cells Devices
    You can connect cameras to DVRs
Allows for Static IP addresses (SIM Assignment)
Address range for dynamic assignment by the drop off box.

## Slide 7: Vmware resources

## Slide 8: Use case – UETN Tech Summit
You have your Inseego Hotspot
  Tethered to your laptop for top performance
Control traffic goes to the UETN core
User traffic goes to your private network and drops off in your location
No need for VPN
You are online at your office with great performance