## Slide 1
Performance Troubleshooting across Networks
Joe Breen
University of Utah
Center for High Performance Computing

## Slide 2
What are User Expectations?
http://fasterdata.es.net/home/requirements-and-expectations/
Notes: Fasterdata Network Requirements and Expectations
http://fasterdata.es.net/home/requirements-and-expectations/

## Slide 3
What are the steps to attain the expectations?
First, make sure the host specs are adequate
  Are you shooting for 1G, 10G, 25G, 40G, 100G?
Second, tune the host
  most are auto-tuning but higher speeds are still problematic
Third, validate network is clean between hosts
Fourth, make sure the network stays clean

## Slide 4
Host specs
Motherboard specs
  Higher CPU speed better than higher core count
  PCI interrupts tie to CPU processor ==> Try to minimize crossing bus between CPU processors
  Storage Host Bus adapters and Network Interface Cards require the correct generation of PCI Express and the correct number of lanes
Notes: http://fasterdata.es.net/science-dmz/DTN/hardware-selection/motherboard-and-chassis/
http://www.tested.com/tech/457440-theoretical-vs-actual-bandwidth-pci-express-and-thunderbolt/
https://fasterdata.es.net/science-dmz/DTN/hardware-selection/motherboard-and-chassis/
http://darkness.codefu.org/wordpress/2005/08/pci-vs-pci-x-vs-pci-express-2/
https://en.wikipedia.org/wiki/PCI_Express#PCI_Express_3.0
https://fasterdata.es.net/science-dmz/DTN/100g-dtn/
https://fasterdata.es.net/science-dmz/DTN/reference-implementation/

## Slide 5
Host specs
PCI bus
  What generation of PCI Express (PCIe) and how many lanes?
    4, 8, and16 lanes possible
      # of lanes supported depends on motherboard and Network Interface Card (NIC)
    Speed of lane depends on generation of PCIe
      PCIe 2 -> 2.5Gb/s per lane including overhead
      PCIe 3 -> 5Gb/s per lane including overhead
Notes: http://www.tested.com/tech/457440-theoretical-vs-actual-bandwidth-pci-express-and-thunderbolt/
https://fasterdata.es.net/science-dmz/DTN/hardware-selection/motherboard-and-chassis/
http://darkness.codefu.org/wordpress/2005/08/pci-vs-pci-x-vs-pci-express-2/
https://en.wikipedia.org/wiki/PCI_Express#PCI_Express_3.0
https://fasterdata.es.net/science-dmz/DTN/100g-dtn/
https://fasterdata.es.net/science-dmz/DTN/reference-implementation/

## Slide 6
Host specs
PCI Implications
  PCIe v2 with 8 lanes and greater for 10G
  PCIe v3 with 8 lanes and greater for 40G
  PCIe v3 with 16 lanes and greater for 100G +
Notes: http://www.tested.com/tech/457440-theoretical-vs-actual-bandwidth-pci-express-and-thunderbolt/
https://fasterdata.es.net/science-dmz/DTN/hardware-selection/motherboard-and-chassis/
http://darkness.codefu.org/wordpress/2005/08/pci-vs-pci-x-vs-pci-express-2/
https://en.wikipedia.org/wiki/PCI_Express#PCI_Express_3.0
https://fasterdata.es.net/science-dmz/DTN/100g-dtn/
https://fasterdata.es.net/science-dmz/DTN/reference-implementation/

## Slide 7
Host specs
Storage subsystem factors
  Local disk
    RAID6, RAID5 or RAID 1+0
    SATA or SAS
    Spinning disk vs SSD
  Network disk
    High speed parallel system vs NFS or SMB mounts,
Notes: Local Storage:
* http://fasterdata.es.net/science-dmz/DTN/hardware-selection/storage/
* https://en.wikipedia.org/wiki/Serial_ATA
* https://en.wikipedia.org/wiki/Serial_Attached_SCSI
* https://en.wikipedia.org/wiki/Solid-state_drive
Network Storage
NFS:
* v3 https://tools.ietf.org/html/rfc1813
* v4.1 https://tools.ietf.org/html/rfc5661
CIFS/SMB:
* https://en.wikipedia.org/wiki/Server_Message_Block
* https://msdn.microsoft.com/en-us/library/windows/desktop/aa365233(v=vs.85).aspx
* https://technet.microsoft.com/en-us/library/cc939973.aspx
Storage Performance:
* http://www.citi.umich.edu/projects/nfs-perf/results/cel/write-throughput.html
Storage performance testers:
* http://beyondtheblocks.reduxio.com/8-incredibly-useful-tools-to-run-storage-benchmarks
* http://www.clustermonkey.net/FileSystems/benchmarking-parallel-file-systems.html
* http://wiki.opensfs.org/Benchmarking_Basics
* https://www.spec.org/sfs2008/press/release.html
Parallel File Systems
* Parallel NFS: http://www.pnfs.com/
* Lustre:http://lustre.org/
* GPFS:
** https://en.wikipedia.org/wiki/IBM_General_Parallel_File_System
** https://www.ibm.com/support/knowledgecenter/en/SSFKCN/gpfs_welcome.html
Multi-tenancy:
* http://whatis.techtarget.com/definition/multi-tenancy
* https://en.wikipedia.org/wiki/Multitenancy
* http://whatis.techtarget.com/definition/multi-tenancy

## Slide 8
Host specs and other
Memory – 32GB or greater
Other factors such as multi-tenancy – how busy is your system?
Notes: Local Storage:
* http://fasterdata.es.net/science-dmz/DTN/hardware-selection/storage/
* https://en.wikipedia.org/wiki/Serial_ATA
* https://en.wikipedia.org/wiki/Serial_Attached_SCSI
* https://en.wikipedia.org/wiki/Solid-state_drive
Network Storage
NFS:
* v3 https://tools.ietf.org/html/rfc1813
* v4.1 https://tools.ietf.org/html/rfc5661
CIFS/SMB:
* https://en.wikipedia.org/wiki/Server_Message_Block
* https://msdn.microsoft.com/en-us/library/windows/desktop/aa365233(v=vs.85).aspx
* https://technet.microsoft.com/en-us/library/cc939973.aspx
Storage Performance:
* http://www.citi.umich.edu/projects/nfs-perf/results/cel/write-throughput.html
Storage performance testers:
* http://beyondtheblocks.reduxio.com/8-incredibly-useful-tools-to-run-storage-benchmarks
* http://www.clustermonkey.net/FileSystems/benchmarking-parallel-file-systems.html
* http://wiki.opensfs.org/Benchmarking_Basics
* https://www.spec.org/sfs2008/press/release.html
Parallel File Systems
* Parallel NFS: http://www.pnfs.com/
* Lustre:http://lustre.org/
* GPFS:
** https://en.wikipedia.org/wiki/IBM_General_Parallel_File_System
** https://www.ibm.com/support/knowledgecenter/en/SSFKCN/gpfs_welcome.html
Multi-tenancy:
* http://whatis.techtarget.com/definition/multi-tenancy
* https://en.wikipedia.org/wiki/Multitenancy
* http://whatis.techtarget.com/definition/multi-tenancy

## Slide 9
Host tuning
TCP Buffers sets the max data rate
  Too small means TCP cannot fill the pipe
  Buffer size = Bandwidth * Round Trip Time
  Use ping for the RTT
Most recent Operating Systems now have auto-tuning which helps
  For high bandwidth, i.e. 40Gbps+ NICs, the admin should double-check the maximum TCP buffer settings (OS dependent)
Notes: http://fasterdata.es.net/host-tuning/background/
Matt Mathis paper

## Slide 10
Host tuning needs info on the network
Determine the Bandwidth-Delay Product (BDP)
  Bandwidth Delay Product = Bandwidth * Round Trip Time
  BDP = BW * RTT
  e.g. 10Gbps*70ms =700,000,000bits = 87,500,000Bytes
BDP determines proper TCP Receive Window
  RFC 1323 allows TCP extensions, i.e. window scaling
  Long Fat Pipe (LFN) – networks with large bandwidth delay.
Notes: Matt Mathis original paper
* http://ccr.sigcomm.org/archive/1997/jul97/ccr-9707-mathis.pdf
TCP Performance and the Mathis equation
* http://www.netcraftsmen.com/tcp-performance-and-the-mathis-equation/
Enabling High Performance Data Transfers
* https://www.psc.edu/services/networking/68-research/networking/641-tcp-tune
TCP Large Window extensions – window scale and Long Fat Pipes * RFC 1323 - https://www.ietf.org/rfc/rfc1323.txt
A User's Guide to TCP Windows (Von Welch)
http://www.vonwelch.com/report/tcp_windows
Sizing Router Buffers (Appenzeller, Keslassy, McKeown)
http://yuba.stanford.edu/techreports/TR04-HPNG-060800.pdf
Internet Protocol Journal -- TCP Performance (Geoff Huston)
* http://www.cisco.com/c/en/us/about/press/internet-protocol-journal/back-issues/table-contents-5/ipj-archive/article09186a00800c8417.html

## Slide 11
Host Tuning
Linux
  Modify /etc/sysctl.conf with
  recommended parameters
Apple Mac
  Modify /etc/sysctl.conf with
  recommended parameters
# allow testing with buffers up to 128MB
net.core.rmem_max = 134217728
net.core.wmem_max = 134217728
# increase Linux autotuning TCP buffer limit to 64MB
net.ipv4.tcp_rmem = 4096 87380 67108864
net.ipv4.tcp_wmem = 4096 65536 67108864
# recommended default congestion control is htcp
net.ipv4.tcp_congestion_control=htcp
# recommended for hosts with jumbo frames enabled
net.ipv4.tcp_mtu_probing=1
# recommended for CentOS7/Debian8 hosts
net.core.default_qdisc = fq
# OSX default of 3 is not big enough
net.inet.tcp.win_scale_factor=8
# increase OSX TCP autotuning maximums
net.inet.tcp.autorcvbufmax=33554432
net.inet.tcp.autosndbufmax=33554432
See Notes section for links with details and description
Notes: Linux:
* http://fasterdata.es.net/host-tuning/linux/
Apple Mac:
* http://fasterdata.es.net/host-tuning/osx/
* https://rolande.wordpress.com/2010/12/30/performance-tuning-the-network-stack-on-mac-osx-10-6/
MS Windows:
* http://www.thewindowsclub.com/window-auto-tuning-in-windows-10
* https://www.speedguide.net/articles/windows-8-10-2012-server-tcpip-tweaks-5077
* MS Win 10 and Server 2016 Powershell Network cmdlets
** https://technet.microsoft.com/en-us/itpro/powershell/windows/netadapter/netadapter
** https://technet.microsoft.com/itpro/powershell/windows/nettcpip/set-nettcpsetting

## Slide 12
Host Tuning
MS Windows
  Show the autotuning status - "netsh interface tcp show global"
  Use Powershell Network cmdlets for changing parameters in Windows 10 and Windows 2016
    e.g. Set-NetTCPSetting -SettingName "Custom" -CongestionProvider CTCP -InitialCongestionWindowMss 6
See Notes section for links with details and description
Notes: Linux:
* http://fasterdata.es.net/host-tuning/linux/
Apple Mac:
* http://fasterdata.es.net/host-tuning/osx/
* https://rolande.wordpress.com/2010/12/30/performance-tuning-the-network-stack-on-mac-osx-10-6/
MS Windows:
* http://www.thewindowsclub.com/window-auto-tuning-in-windows-10
* https://www.speedguide.net/articles/windows-8-10-2012-server-tcpip-tweaks-5077
* MS Win 10 and Server 2016 Powershell Network cmdlets
** https://technet.microsoft.com/en-us/itpro/powershell/windows/netadapter/netadapter
** https://technet.microsoft.com/itpro/powershell/windows/nettcpip/set-nettcpsetting

## Slide 13
What does the Network look like?
What bandwidth do you expect?
How far away is the destination?
  What is the round trip time that ping gives?
Are you able to support jumbo frames?
  Send test packets with the "don't fragment bit set
    Linux or Mac: "ping -s 9000 -Mdo <destination>"
    Windows: "ping -l 9000 -f <destination>"
Notes: Matt Mathis original paper
*
PSC pages
* https://www.psc.edu/services/networking/68-research/networking/641-tcp-tune
* http://www.cisco.com/c/en/us/about/press/internet-protocol-journal/back-issues/table-contents-5/ipj-archive/article09186a00800c8417.html

## Slide 14
What does the Network look like?
Do you have asymmetric routing?
  Traceroute from your local machine gives one direction
  Are you able to traceroute from the remote site?
  Are they mirrors of each other?
Notes: Matt Mathis original paper
*
PSC pages
* https://www.psc.edu/services/networking/68-research/networking/641-tcp-tune
* http://www.cisco.com/c/en/us/about/press/internet-protocol-journal/back-issues/table-contents-5/ipj-archive/article09186a00800c8417.html

## Slide 15
What does the Network look like?
Determine the Bandwidth-Delay Product (BDP)
  Bandwidth Delay Product = Bandwidth * Round Trip Time
  BDP = BW * RTT
  e.g. 10Gbps*70ms =700,000,000bits = 87,500,000Bytes
BDP determines proper TCP Receive Window
  RFC 1323 allows TCP extensions, i.e. window scaling
  Long Fat Pipe (LFN) – networks with large bandwidth delay.
Notes: Matt Mathis original paper
* http://ccr.sigcomm.org/archive/1997/jul97/ccr-9707-mathis.pdf
TCP Performance and the Mathis equation
* http://www.netcraftsmen.com/tcp-performance-and-the-mathis-equation/
Enabling High Performance Data Transfers
* https://www.psc.edu/services/networking/68-research/networking/641-tcp-tune
TCP Large Window extensions – window scale and Long Fat Pipes * RFC 1323 - https://www.ietf.org/rfc/rfc1323.txt
A User's Guide to TCP Windows (Von Welch)
http://www.vonwelch.com/report/tcp_windows
Sizing Router Buffers (Appenzeller, Keslassy, McKeown)
http://yuba.stanford.edu/techreports/TR04-HPNG-060800.pdf
Internet Protocol Journal -- TCP Performance (Geoff Huston)
* http://www.cisco.com/c/en/us/about/press/internet-protocol-journal/back-issues/table-contents-5/ipj-archive/article09186a00800c8417.html

## Slide 16
How clean does the network really have to be?
http://fasterdata.es.net/network-tuning/tcp-issues-explained/packet-loss/
Notes: ES net TCP tuning
http://fasterdata.es.net/network-tuning/tcp-issues-explained/packet-loss/

## Slide 17
How do I validate the network?
Measurement!
  Active measurement
    Perfsonar – www.perfsonar.net
    Iperf - https://github.com/esnet/iperf
    Nuttcp - https://www.nuttcp.net/Welcome%20Page.html
  Passive measurement
    Nagios, Solarwinds, Zabbix, Zenoss
    Cacti, PRTG, RRDtool
    Trend the drops/discards
Notes: Perfsonar
http://www.perfsonar.net
Iperf
https://github.com/esnet/iperf
Nuttcp
https://www.nuttcp.net
Nagios

## Slide 18
How do I make sure the network is clean on a continual basis?
Design network security zone without performance inhibitors
Set up appropriate full bandwidth security
  Access Control Lists
  Remotely Triggered Black Hole Routing
Setup ongoing monitoring with tools such as perfSONAR
  Create a maddash dashboard

## Slide 19
Set up a performance/security zone
Science DMZ architecture is a dedicated performance/security zone on a campus
http://fasterdata.es.net/science-dmz/motivation/
Notes: Science DMZ
http://fasterdata.es.net/science-dmz/motivation/
Science DMZ: A Network Design Pattern for Data-Intensive Science
https://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf

## Slide 20
Use the right tool
Rclone - https://rclone.org/
Globus - https://www.globus.org/
FDT - http://monalisa.cern.ch/FDT/
Bbcp - http://www.slac.stanford.edu/~abh/bbcp/
Udt - http://udt.sourceforge.net/

## Slide 21: 100G Host, Parallel Streams: no pacing vs 20G pacing
Techniques such as Packet Pacing
Credit: Brian Tierney, Nathan Hanford, Dipak Ghosal https://www.es.net/assets/pubs_presos/packet-pacing.pdf
Notes: Optimizing Data Transfer Nodes using Packet Pacing
https://www.es.net/assets/pubs_presos/packet-pacing.pdf

## Slide 22
Techniques such as Packet Pacing
Credit: Brian Tierney, Nathan Hanford, Dipak Ghosal https://www.es.net/assets/pubs_presos/packet-pacing.pdf
Notes: Faster Data Packet pacing (ESnet)
https://fasterdata.es.net/host-tuning/packet-pacing/

## Slide 23
Not just about research
Troubleshooting to the cloud is similar
  High latency, with big pipes
    Latency is not just to the front door but also internal to the cloud providers
  Example: Backups to the cloud are a lot like big science flows

## Slide 24
Live example troubleshooting using bwctl on perfsonar boxes
Bwctl -s <server_ip> -c <client_ip>

## Slide 25
References:
See Notes pages on print out of slides for references for each slide